## Slide 1: Predicting sleep quality using accelerometer data from wearable devices
Casandra Philipson

## Slide 2: Visualizing Raw Data

## Slide 3: Digital Signal Processing
100Hz wrist-worn data-logging device
Applied a 1st order Butterworth IIR filter
Bandwidth 3-11 Hz
Remove noise present in the data set and to normalize raw x, y, and z measurements.

## Slide 4: More Feature Engineering
run.sd – Running Standard Deviation (always double the metric feature window)
int_mean – Interval mean
int_max – Interval maximum
int_min – Interval minimum
int_sd – Standard deviation within the interval
range – Interval range (max – min)
ratio – Interval ratio (max / min)
int_RMS – Root mean squared of the interval
bfz.absolute – Absolute value vector of the normalized uniaxial z axis data (bf.z)
Fast Fourier transform (frequency and magnitude)
Baseline activity predictions based on movement

## Slide 5: Sleep Disorders and Signal
Sleep disorders don’t increase variability!
REM (as expected) little movement since you’re body is paralyzed

## Slide 6: Sleep Disorders and Sleep Quality
Time spent in different sleep phases does not appear to be affected by sleep disorder

## Slide 7: Predicting Sleep/Wake Cycles
Personalized predictions have >80% accuracy!

## Slide 8: Model Performance Diminishes as Window Time Increases
Assessing features in short time frames lends better predictive value